## Slide 1: Computationally Efficient Methods for Stochastic Generator Expansion Planning
Vijay Kumar
Industrial Engineering Department
The Pennsylvania State University

## Slide 2: What is Generator Expansion Planning?
Problem Statement
  Minimize Net Present Value
  Subject to
    Demand Constraints
    Environment Constraints
Variables
  Investment (New Capacity of each technology)
  Generation (Generation level of each technology)
Notes: The main question for energy utilities and Independent system operators was to determine the amount of renewable energy integration into the power grid. This motivates the question of what generator types to build in the future?

## Slide 3: Problem Framing
Stage 1:
Choose investment
mix & operate for 10 yrs
Stage 2:
Choose investment
mix & operate for 10 yrs
Stage 3:
Choose investment
mix & operate for 30 yrs
Observe Fuel Prices,
Technology Costs,
& Policy Discussions
Observe Cumulative
Carbon Cap, fuel prices,
technology costs
Technologies:
Nuclear
Coal
NG-CCGT
NG-CT
Coal-CCS*
Wind*
Solar (PV)*
Uncertainties:
Cumulative Carbon Cap at end of Stage 3
Natural Gas Price
Nuclear Capital Costs
Wind Capital Costs
Solar Capital Costs
Coal-CCS Capital Costs
Notes: The stochastic dynamic program solution has been present Bellamn invented in 1960

## Slide 4: Classic Dynamic Programming Solution Methods
Loop over states S
Loop over time t / iterations n
Loop over decisions X
Loop over random shocks W
Algorithmic Framework
Suffers from Curse of
Dimensionality
Objective of the Stochastic Problem
Choose RE(t) to maximize Bellman Value (Total Reward) in each time period:
Vt*(St) = max(Ct(St, REt) + E[Vt+1(St+1)|St, REt])
μ(t)
Decision
State
Decision
State
T=1
Decision
T=2
State
T=3

## Slide 5: What is the solution? ADP
Don’t visit ALL states exhaustively
  Sample states
Don’t test EVERY exogenous information signal
  Sample the information
MAX E{f(x)} is hard
  Break into two steps:
  Deterministic Optimization: Best action for a sample state, sample signal, and estimate of the value function
  Stochastic Simulation: Get a better estimate of the expected value for a sample state and it’s best action
Challenges
  Obtain a good low dimensional form of the value function
  How to Sample efficiently ?

## Slide 6: Double Pass ADP Algorithm
Step 0: Initialize Vt0, n, S01
Step 1: Choose sample path wn
Step 2: loop over t=0 to T
Step 2a: Solve:
Step 2b: Update States
Step 3: Loop over t=T, T-1, …, 1
Step 3a: Compute vtn using xtn from forward pass
Step 3b: Update value function approximations
Step 4: n=n+1; if n<=N go to Step 1
Step5 : Return Value functions Vtn

## Slide 7: How to Sample efficiently? Exploration-Exploitation tradeoff
Objective: Gather enough information to make best decisions overall.
Exploitation: should I stick with what I know and find a good policy w.r.t. this knowledge?
  at risk of missing out on a better reward somewhere
Exploration: should I look for states w/ more reward?
  at risk of wasting time & getting some negative reward
Another Idea : Obtain a set of samples using modified version of accept reject with acceptance ratio as

## Slide 8: Comparison to other algorithms
Complete Exploration : Choose an action randomly
Complete Exploitation : Choose an action to maximize the value function approximation Vt
e- greedy : Choose to explore with probability and exploit with probability 1-
Knowledge Gradient Algorithm : Choose an action that maximizes
Bilinear Value function approximation was used and each algorithm was run for 40 hours.

## Slide 9: Test Problem and Results
Test Problem : 3 Time Periods in increments of 20 years, 4 Technologies and 2 uncertainties in Fuel Prices and Cost of Carbon.
Conclusion and Future Work
Comparison of the solution to Exact Dynamic
Programming or Stochastic Optimization solution.
Testing of this methodology to other ADP
frameworks such as Inventory, Cart Pole or Chess.